Consider the following simple network (very similar to example in talk, just with longer and more fiber links):

Use the tables below to develop pricing for a network based on gigabit Ethernet and 10gig Ethernet links for all fiber types (OM1, OM2, OM3, OM4, and OS2).

| Types of Optical Interfaces |  |
| --- | --- |
| Standard | Speed | Supported Fiber | Cost |
| 1000baseSX | 1000Mbs | MM | $171 |
| 1000baseLX/LH | 1000Mbs | MM or SM | $300 |
| 10GbaseSR | 10Gbs | MM | $780 |
| 10GbaseLRM | 10Gbs | MM | $930 |
| 10GbaseLR | 10Gbs | SM | $3,000 |
| 10GbaseER | 10Gbs | SM | $6,360 |
| Distances Supported by Interfaces |  |  |  |
| Standard | OM1 | OM2 | OM3 | OM4 | OS2 |
| 1000baseSX | 275m | 550m | 1km | 1.1km | No |
| 1000baseLX/LH | 500m | 500m | 500m | 500m | 10km |
| 10GbaseSR | 33m | 82m | 300m | 550m | No |
| 10GbaseLRM | 220m | 220m | 220m | 220m | No |
| 10GbaseLR | No | No | No | No | 10km |
| 10GbaseER | No | No | No | No | 40km |

| Cost of Fiber |  |
| --- | --- |
| Fiber Type | Budget Cost per km |
| OM1 | $3,087 |
| OM2 | $2,203 |
| OM3 | $3,739 |
| OM4 | $4,861 |
| OS2 | $2,150 |

Here are some worksheets to use.

What is the total installed fiber length?       3300 m

| Cost of 1 Gigabit Network |  |  |
| --- | --- | --- |
| Fiber Type | Fiber Cost | Optics Used | Optics Cost | Total Cost |
| OM1 | 3087*3.3= $10,220.10 | Can’t do gigabit on OM1 on links over 275m |  |  |
| OM2 | 2203*3.3= $7,269.90 | Can’t do gigabit on OM2 on links over 550m |  |  |
| OM3 | 3739*3.3= $12,338.70 | 12 x 1000baseSX | 12*171=$2,052 | $1,4390.70 |
| OM4 | 4861*3.3= $16,041.30 | 12 x 1000baseSX | 12*171=$2,052 | $ 18,093.30 |
| OS2 | 2150*3.3= $ 7,095.00 | 12 x 1000baseLX | 12*300=$3,600 | $ 10,695.00 |

| Cost of 10 Gigabit Network |  |  |
| --- | --- | --- |
| Fiber Type | Fiber Cost | Optics Used | Optics Cost | Total Cost |
| OM1 | 3087*3.3= $10,220.10 | Can’t do gigabit on OM1 on links over 220m |  |  |
| OM2 | 2203*3.3= $7,269.90 | Can’t do gigabit on OM2 on links over 220m |  |  |
| OM3 | 3739*3.3= $12,338.70 | Can’t do gigabit on OM3 on links over 300m |  |  |
| OM4 | 4861*3.3= $6,041.30 | Can’t do gigabit on OM4 on links over 550m |  |  |
| OS2 | 2150*3.3= $ 7,095.00 | 12 x 10GbaseLR | 12*3,000=$36,000 | $43,095.00 |